## Examples of Telemetry Data and Aerial Images

For more information and documents related with the project, please use the following contact information:

URL: http://paloma.isr.uc.pt/diva/ Contact person: Luiz Mirisola Email: lgm@isr.uc.pt

Mobile Robotics Laboratory Institute of Systems and Robotics Department of Electrical and Computer Engineering Coimbra University Pinhal de Marrocos, Pólo II 3030 COIMBRA – Portugal Tel. +351 239 796 219 · Fax 351 239 406 672

Project

DIVA – Autonomous Airship

for Aerial Surveillance
 Aerial Autonomous Systems – Control, Mapping, Embedded Systems.

Joint Project of ISR-Coimbra, IST-Lisbon and Univ. do Minho,  2004 –  2006

http://paloma.isr.uc.pt/diva/

Partners:

Sponsors:

# Main Goals

- Design of a solution based on a small size airship as an aerial stable platform

- For semi-autonomous monitoring

- For surveillance mission

Partners Tasks

Each partner was responsible for one investigation area:

| Instituto de Engenharia Mecânica IDMEC / IST | Instituto de Sistemas e Robótica ISR Coimbra / FCTUC | Centro Interdisciplinar de Tecnologias de Produção e Energia UM |
| --- | --- | --- |
| Av. Rovisco Pais, 1 1049-001 Lisboa | Dept. Eng. Electrotécnica e de Computadores Univ. de Coimbra, Pólo 2 3030-290 Coimbra | Dept. Eng. Mecânica, Escola de Engenharia 4800 Guimarães |
| Main tasks: overall coordination, modelling, simulation and control | Main tasks: systems integration, airborne vision and surveillance | Main tasks: aerodynamic characterization and modelling |

System architecture

The onboard system:

Instrumented aero model: GPS, IMU, Wind Sensor, Motor Speed

Capture video synchronized with sensor data

Next: On board control loop via PC104 CPU

AIRSHIP

- on-board PC is PC104+.

- Radio Control Receiver

- Actuators and flight control:

  - Internal combustion engines

  - Propellers with 90º vectorization

  - Helium valve (emergency landing)

- Localization and navigation:

  - GPS

  - Inertial and magnetic sensors

  - Wind sensor

  - Motor Speed

- Mission specific sensors:

  - High resolution camera

  - Video synchronized w/ sensor data

GROUND CONTROL

- Ground Station PC

  - DGPS

- Wireless Ethernet link

  - Monitoring & logging of airship telemetry data

  - CORBA as a middleware

# Text boxes

Inertial System

calibrated with

on-board Camera

(i.e., rotation between both frames is known)

The Wind Sensor

- Barometric Pressure

- Air Pressure

- Attack Angles

Aerial images synchronized with sensorial data

- Datasets for mapping and tracking tasks

The inertial data is used to project an aerial image into the ground plane

Telemetry obtained in a flight test from GPS and pressure sensors